Limen Alpha
Programmer's manual
* When accessing to control registers, unused register index must have zero value.
Dominik Salvet, 2016

# A brief description of Limen Alpha
Limen Alpha is processor architecture with following characteristics:
- 16-bit width,
- Von Neumann type,
- RISC type,
- dual-core variant,
- can address up to 64 kDB.
# Memory model
It's used physically addressed flat memory model - every address used in instruction is equal address that will appear on the address bus. Memory address space also contains mapped I/O device and is shared for both processor cores.
# Register file
Architecture defines eight general purpose registers. However, register R0 represents always zero value, write to this register is ignored. There is also IP register that holds address of actual executed instruction and some control registers.
# List of instructions

- SLU - set if less unsigned
- SL - set if less
- ADD - addition
- LL - load linked
- LD - load
- SC - store conditional
- ST - store
- OR - logical disjunction
- ORN - logical disjunction not
- AND - logical conjunction
- ANDN - logical conjunction not
- XOR - exclusive logical disjunction
- SLL - shift left logical
- SRL - shift right logical
- SRA - shift right arithmetic
- SUB - subtraction
- RTC - register to control
- CTR - control to register
- LI - load immediate
- LIS - load immediate scaled
- LIL - load immediate low
- LIH - load immediate high
- JNE - jump if not equal
- JE - jump if equal
- JL - jump if less
- JLE - jump if less or equal
- JG - jump if greater
- JGE - jump if greater or equal
- JWL - jump with link
# Instruction formats
Bits with indexes 13 to 15 of every instruction word determine its instruction format. Instructions that are in the same instruction format are often executed very similarly.
## Introducing
The following concept [s]imm<x>, where <x> is natural number, represents numbers:
- imm<x> - from 0 to 2x - 1,
- simm<x> - from -2(x - 1) to 2(x - 1) - 1.
imm<x> format and natural numbers of simm<x> format can be expressed in various radix:
- Decimal - <digits(0-9)> or <digits(0-9)>D or <digits(0-9)>d,
- Hexadecimal - <digits(0-F or 0-f)>H or <digits(0-F or 0-f)>h,
- Octal - <digits(0-7)>O or <digits(0-7)>o,
- Binary - <digits(0,1)>B or <digits(0,1)>b.
Negative numbers must be expressed only in one of decimal radix formats.
## Arithmetic with immediate value
Instructions of arithmetic type with 5-bit signed immediate value. This value is in two's complement format.
Instruction word structure

List of instructions

## Transfer with immediate displacement
The only format that allows access to memory and perform synchronization matters. The final memory address is result of sum register value and 5-bit signed immediate value. This value represents displacement from register value.
Instruction word structure

List of instructions

## Logic with immediate value
This instruction format can perform logic operations with 4-bit immediate value, which is first of all extended with zeros to 16-bit width. Instruction format also includes logical and arithmetic shift instructions.
Instruction word structure

List of instructions

## Arithmetic, logic and control with registers
Instruction format can perform all previous logical and arithmetic instructions. Moreover there is a subtraction. This instruction format uses only registers as operands. There are also instructions for access to control registers.*
Instruction word structure

List of instructions

## Load immediate value
Instructions that load 8-bit unsigned immediate to registers. There are two mods: 1) load 8-bit immediate direct/scaled to register, 2) merge 8-bit immediate with lower/higher part of register.
Instruction word structure

List of instructions

## Conditional jump with immediate displacement
Provides the only way to realize conditional branching. The final address of success jump is displacement of actual instruction address (IP register value). For this reason, instruction word contains 7-bit signed immediate value. Conditional branch is always result of compare register value and zero.
Instruction word structure

List of instructions

## Unconditional jump with immediate displacement
Includes only one instruction - instruction for realize unconditional jumps and calling functions in program. The first operand is register into which is saved return address (incremented IP register value). Using register R0 if don't needed to save return address. The second operand is 10-bit signed immediate in which range can be jump performed.
Instruction word structure

List of instructions

## Unconditional jump with registers
Another format for implement unconditional jumps and calling functions. However, opposed to previous format, the jump address is register value that is used as a pointer, save return address is also possible.
Instruction word structure

List of instructions

# Instruction processing
Each instruction takes six clock signals and is overlapped in two phases with a following instruction. So every four clock signals is completed one instruction on the processor core. A pair of processor cores are running together without any stalls.

## Instruction phases
- NEXT - write new instruction address to IP register
- LOAD - read instruction from memory
- FETCH - fetch instruction from memory bus
- ALU - perform arithmetic or logic operation
- MEM - access to memory / control registers
- REG - write result to register
# Control registers
Control registers are auxiliary core registers that provides way to use some extra functionality of core.

## MSR - Machine Status Register
ID - Interrupt Disable
Reset value
ID - 1, others - 0
## SIP - Saved Instruction Pointer
When interrupt occurs, the return address is saved here.
## PRNG - Pseudorandom number generator
Every clock is generated a new pseudorandom number, which can be read from this register. All program writes to this register are ignored.
Reset value
Core 0 - 0xFFFF, Core 1 - 0xDDD4
Algorithm
For generate pseudorandom numbers is used linear-feedback shift register Galois type.
Polynomial used:	x^16 + x^15 + x^14 + x^12 + x^11 + x^9 + x^8 + x^7 + x^5 + x^2 + 1
# Interrupt processing
One instruction that follows RTC instruction can not be interrupted and always will be executed. After accept interrupt, further interrupts are automatically disabled.

0
1
RTC
0

3
1
...
RTC
JWL

4
...

Main program
Interrupt routine
Interrupt enable
Interrupt request
# Cores synchronization
Synchronization mechanism is used when core requires exclusive access to shared data. Before program gets exclusive access to this data, must use some form of synchronization primitives. The very access to this data is done in “critical section”.
## Mechanism to achieve synchronization
To realize synchronization of access to shared data, there are two instructions LL and SC. Indeed, this instructions provide a way to implement higher level constructions for synchronization.
## Behavior of LL and SC instructions
In the processor there are two bit registers called Link bit and Link core. When LL instruction is executed, Link bit is set to one and Link core is set to core's index which executed this instruction. When SC instruction is executed, it will be indicate whether it was successful or not with write value to register (1 - success, 0 - fail). SC will be successful only if Link bit is set to one and Link core is equal to index of core that is executing this instruction. If this condition is met, write to memory is approved and performed and Link bit is set to zero. Otherwise write to memory is dismissed and Link bit doesn't change.
## Lock implementation example
This example uses Test and test-and-set method with active waiting.
; R1 - lock address

DEF unlock_st 0
DEF lock_st 1

test:	LD R2, R1, 0
JNE R2, test

test_and_set:	LI R2, lock_st
LL R3, R1, 0
JNE R3, test
SC R2, R1, 0
JE R2, test_and_set

locked:	…
# Program example
; == Call procedure ==
; test call procedure via register value as pointer

;address	mnemonic	binary	C like
; void main() {
; do {
 0	:	LI R4, 0	1000000000000100	; R4 = 0;
 1	:	LIH R4, 4	1000000010011100	; R4 = 1024;
 2	:	SRL R5, R4, 3	0101100011100101	; R5 = R4 >> 3;
 3	:	JWL R6, R5	1110000000101110	; <R5>(); //128
 4	:	LIL R4, 0	1000000000010100	; R4 &= 0xFF00;
 5	:	JWL R0, R4	1110000000100000	; } while(1);
; void 128() {
 128	:	SUB R4, R4, R5	0111010101100100	; R4 -= R5;
 129	:	SRL R4, R4, 1	0101100001100100	; R4 >>= 1;
 130	:	LIH R4, 0	1000000000011100	; R4 &= 0x00FF;
 131	:	JWL R0, R4	1110000000100000	; //“JMP R4” (192)
;
 192	:	JWL R0, R6	1110000000110000	; return;
; }
; }
The program is only for demonstrate the possibilities. Used algorithm is not intended to be optimized.
# List of Symbols and Abbreviations

DB	Double byte
IP	Instruction pointer
Rz, Ry, Rx	General purpose register indexes
LC	Link core
AC	Actual core
LB	Link bit
Ci	Control register index
DEF	Define